## Slide 1
Homogenizer

## Slide 2
Drive shaft
Shaft tube
Teflon seal
Stator
Rotor
1
3
5
2
4

## Slide 3
1.
2.
Insert the drive shaft into shaft tube
Position teflon seal over the shaft sleeve

## Slide 4
3.
Screw the rotor onto the drive shaft and turn clockwise using the flat key as a counter tool.
4.
Screw the stator onto the shaft tube, turning counterclockwise

## Slide 5
5.
Open the knurled screw (pos. 2)
Insert the dispersing element (pos. 1)
Screw the knurled screw tight (pos. 2)
2
1

## Slide 6
6.
Turn on the divice
Adjust the rpm